## Slide 1: Network Topologies
Class 12 Computer Science/Information Technology

## Slide 2: Introduction to Network Topologies
A network topology refers to the arrangement of various elements (links, nodes) in a computer network.
Types:
- Physical Topology
- Logical Topology

## Slide 3: Types of Network Topologies
Point-to-Point Topology:
- Direct connection between two devices.
- Example: USB connection.

## Slide 4: Bus Topology
Description:
- Single central cable (bus) connects all devices.
- Data travels in both directions.
Advantages:
- Cost-effective and easy to install.
Disadvantages:
- Limited cable length and bandwidth.
- Difficult to troubleshoot.

## Slide 5: Star Topology
Description:
- All devices are connected to a central hub.
Advantages:
- Easy to add/remove devices.
- Centralized control.
Disadvantages:
- Single point of failure (hub).

## Slide 6: Ring Topology
Description:
- Devices are connected in a circular manner.
- Data travels in one direction (unidirectional) or both (bidirectional).
Advantages:
- Equal access to resources.
Disadvantages:
- Failure in one node affects the entire network.

## Slide 7: Mesh Topology
Description:
- Every device is connected to every other device.
Advantages:
- High fault tolerance.
- Reliable.
Disadvantages:
- Expensive and complex to set up.

## Slide 8: Tree Topology
Description:
- A combination of star and bus topologies.
- Devices are organized hierarchically.
Advantages:
- Scalable and easy to manage.
Disadvantages:
- Higher cost due to cabling.
- A failure at the root affects the entire topology.

## Slide 9: Fully Connected Topology
Description:
- Every node is directly connected to every other node.
Advantages:
- Maximum reliability and fault tolerance.
- High-speed data transfer.
Disadvantages:
- Extremely expensive and complex.
- Not scalable for large networks.

## Slide 10: Hybrid Topology
Description:
- Combination of two or more topologies.
Advantages:
- Flexible and scalable.
Disadvantages:
- Complex to design and implement.

## Slide 11: Comparison of Topologies
Comparison Factors:
- Cost
- Complexity
- Scalability
- Fault Tolerance
- Examples

## Slide 12: Conclusion
Key Points:
- Network topology defines structure.
- Different topologies suit different needs.
Importance of selecting the right topology.

## Slide 13: Thank You
Feel free to ask questions!